## Slide 1: Convergence and accuracy of coupled FV/MC codes
M. Baelmans
With research results and input from
P. Börner, W. Dekeyser, K. Ghoos,
N. Horsten, G. Samaey, T. Van Oevelen
WPCD-meeting 10-12 December 2014, Garching, Germany
Notes: 30 minutes

## Slide 2: Introduction
B2/B2.5
False time stepping
Dual time stepping (nstages)
Coupling
Full Monte Carlo
MC+ Short Cycle
Robbins-Monro
EIRENE
Random noise
Correlated sampling
Transient or not
Interpretation of results
One single solution vs. averaged solution
 48 possible combinations and multiple scenarios
= Present ITER choice

## Slide 3: Introduction
GOAL Getting accurate results as fast as possible
OR Quickly getting results as accurate as possible
Starting point = EFDA-report on short cycle
Run time is same for Correlated Sampling and Full MC
Short cycle speed-up factor 5-100 depending on case
Questions: Which procedure to invest in?
Based on error assessment
Debottleneck simulations w.r.t. accuracy vs. run time
 Goal-oriented simulations
Towards ITER/DEMO-relevant conditions
 What kind of errors are we looking at?

## Slide 4: Introduction
Model equations
Convergence
error
Fluid equations
Kinetic
equations
Data processing
Averaging over:
iterations
OR independent runs
Discretize
Finite
Volume
Monte Carlo
Iterate /
Solve
False time steps
Non-linear set of equations
Launch particles at targets
Track particles
Discretization error
Statistical
error
Correlation error
Modelling error
Assume steady state
Systematic error
Statistical error
nit
nt
nr

## Slide 5: Content
A framework for error assessment
First applications of error assessment and code speed-up
Additional attempts for code speed-up
Towards more ITER-relevant cases
Perspectives

## Slide 6: A framework for error assessment
Trends in error contributions
Error assessment possibilities

## Slide 7: Errors at a glance
Simple case with reference solution
  kinetic equation (1D-x, 0D-v) is solved with FV at a very fine grid
  C=0; R = 0.99; T = 40 eV, 10 cm q length
Why do the errors not decrease with nt?
Upstream
Target
ions
neutrals

## Slide 8: Errors at a glance
Eliminate the discretisation error by comparing with solution at coarse FV-grid for both equations
Reference grid: nx = 9,900
Grid in use nx = 99

## Slide 9
Use of grid refinement?
For FV-FV:
 Unfeasible (FV for neutral model when higher dimensions is not possible)
For FV-MC:
Possible with high number of MC particles but impractical
  In this case 10,000 particles and 500 runs used to obtain small statistical errors
  # grid cells: 11-33--99
  and
  Uncertainty ranges (rel.): for ni [0.93-1.13]; up [0.83-1.22]; nn [0.84-1.20]
Fast estimate: Run plasma equations with constant/scaled sources obtained from the finest grid
 All methods lead to same order of magnitude for
Determination of discretization errors

## Slide 10: Errors when correlation sampling
B2/B2.5
False time stepping
Dual time stepping (nstages)
Coupling
Full Monte Carlo
MC+ Short Cycle
Robbins Monro
EIRENE
Random noise
Correlated sampling
Transient or not
Interpretation of results
One single solution vs. averaged solution
!!!!

## Slide 11
Correlation error
if mean of multiple CS simulations,
nt: the number of MC particles
independent of nr and discretization
Statistical error
with nr = number of CS simulations and
the standard deviation of from 1 run
Convergence error
≈ 0
Converged up to machine accuracy, otherwise
determined from convergence rate
Errors when Correlated Sampling (CS)

## Slide 12
All error contributions can be determined
Plasma density
Error when Correlated Sampling (CS)
O(nt-1)
O(m)
O(nt-1/2nr-1/2)
O(Dxp)

## Slide 13: Errors when random noise MC
B2/B2.5
False time stepping
Dual time stepping (nstages)
Coupling
Full Monte Carlo
MC+ Short Cycle
Robbins Monro
EIRENE
Random noise
Correlated sampling
Transient or not
Interpretation of results
One single solution vs. averaged solution
Too large

## Slide 14
Statistical error
educated guess via autocorrelation functions
with :number of independent samples during iterations and the number of iterations
governing the correlation time
Convergence error
≠0
Only one timestep with relaxation is performed when random noise is renewed
Errors when random noise MC
Correlation error
educated guess via residuals of averaged values
~ 1/nt if mean over fluctuating parameters is taken,
when convergence error is sufficient low
with nt: the number of MC particles
independent of nit and discretization

## Slide 15
Errors when random noise MC
Autocorrelation function of the output signal is defined as:
with
Interpretation:
RN makes use of more particles during a correlated time ( ↓)
RN: less MC result in independent samples ( ↓ ↑)
CS
RN
RM

## Slide 16: Errors when Robins-Monro (RM)
B2/B2.5
False time stepping
Dual time stepping (nstages)
Coupling
Full Monte Carlo
MC+ Short Cycle
Robbins Monro
EIRENE
Random noise
Correlated sampling
Transient or not
Interpretation of results
One single solution vs. averaged solution
The final state is taken as solution

## Slide 17
Convergence error
≠0
Only one timestep with relaxation is performed when random noise is renewed and averaged by RM
Errors when Robbins-Monro (RM)
Correlation error
educated guess via residuals of averaged values?
~ 1/nt if mean over fluctuating parameters is taken,
when convergence error is sufficient low
with nt: the number of MC particles
independent of nit and discretization?
 Very low value due to huge damping
Statistical error
? not yet interpreted!
The error contributions are not yet fully understood

## Slide 18: Conclusions
The numerical error, excluding the discretization error, can be written as:
For CS these contributions can be estimated ( )
For RN we can apply an educated guess (two lines: ; )
For RM no procedure (yet)
                 measures can be taken
                now to optimize numerical parameters
RM*
CS
RN

## Slide 19: First applications of error assessment and speed-up
Optimal numerical parameters for 1D case
Error assessment for B2-EIRENE test case

## Slide 20: Optimal CPU-error performance
CS: machine accuracy is not required
Convergence error at it is:
For this case (use of simple SC):
only 5 MC needed for convergence to

## Slide 21: Optimal CPU-error performance
Take
Take 
Find optimal values for
CPU | Error CS | nt CS | n CS | Error RN | nt RN | n RN
2e4 | 1.0e18 | 4e3 | 1 | 1.2e18 | 7 | 46
5e4 | 6.7e17 | 1e4 | 1 | 7.1e17 | 14 | 64
1e4 | 4.9e17 | 1e4 | 2 | 5.0e17 | 25 | 75
2e4 | 3.6e17 | 1e4 | 4 | 3.5e17 | 42 | 94
5e5 | 2.4e17 | 1e4 | 10 | 2.3e17 | 88 | 117
1e6 | 1.9e17 | 1e4 | 20 | 1.7e17 | 147 | 145
2e6 | 1.5e17 | 1e4 | 40 | 1.3e17 | 259 | 168
CS: nt,max = 1e4  take nt as high as possible
RN: first 1000 iterates cannot be used
CPU is expressed in total MC particles

## Slide 22: First applications of error assessment and speed-up
Optimal numerical parameters for 1D case
Error assessment for B2-EIRENE test case

## Slide 23: Error assessment with B2-EIRENE
First results from B2-EIRENE runs with CS, simple case
40 runs on each grid:
11x20, 140x28, 200x40, 400x80
# = 140,000 and 35,000
wall
Plasma
core
target
target
10 m
10 cm
recycling
Major radius = 2-6 m
B
Plasma flow
Well enough converged?
from 40 test, more than 30 converged to machine accuracy, 10 other excluded

## Slide 24: Error assessment with B2-EIRENE
First results from B2-EIRENE runs with CS, simple case
Status:
enough correlated runs
not yet accurate order detection (p)
wall
Plasma
core
target with R = 0.3
10 m
10 cm
recycling
Major radius = 2-6 m
(distance to torus center)
B
Plasma flow
target with R = 0.3
ni
up
100x20
400x80

## Slide 25: Additional improvements
Neutral velocity based short cycle
Residual-based time-stepping

## Slide 26: Neutral velocity based short cycle model
Use of more advanced short cycle (keeping vn constant)
First results indicate even smoother convergence
A certain critical SC number is reached for convergence
To be further test in B2-EIRENE
1D test case

## Slide 27: Residual-based time-stepping
Use of residual-based time-stepping during SC?
B2-EIRENE test case
Once the convergence is exp. the speed-up is very strong
Constant time step
Time step ~ 1/Res when Res < 1e-3

## Slide 28: Towards more ITER-relevant cases
Test cases and strategy
1D OSM-ITER

## Slide 29: Test cases and strategy
Upstream
Target
ions
neutrals
wall
Plasma
core
target
target
10 m
10 cm
recycling
Major radius = 2-6 m
B
Plasma flow
ITER
TOY PROBLEM
1D-x & 0D/1D-v
ITER
B2-EIRENE
2D-x & 3D-v
SLAB
B2-EIRENE
2D-x & 3D-v
ITER 2011
OSM
1D-x & 1D-v

## Slide 30: ITER 2011 - OSM
0,5 m
Fluxtube from ITER 2011
Consider 1 flux tube from a B2-EIRENE run

## Slide 31: ITER 2011 - OSM
Start from B2-EIRENE run
Start with B2-plasma profiles for unknown quant.
  E.g. take Te and Ti from B2-EIRENE along a flux tube
  OSM-approach: get radial transport from B2-EIRENE
  Solve only ni, ui and fn
Essential features
  Flux tube expansion and pitch
  Gas puff, radial transport via C, pumping via R
  Atomic processes via T
with

## Slide 32: ITER 2011 - OSM
B2-EIRENE used to find ni and up in 1D OSM case
next step leaving sources free is in progress

## Slide 33: ITER 2011 - OSM
1D model:
with S and T from B2-EIRENE on coarse and fine grid
changes in profile near target indicate profiles
are sensitive to grid refinement
exact = 6,000 cells
B2 = 9 grid cells

## Slide 34: Further perspective

## Slide 35: Further perspectives
Investigate the cause of convergence failure for correlated sampling in 2D test runs and study improved techniques for correlated sampling (e.g. double background, filtering techniques
Make use of error framework to further elaborate (optimize) the most favorable short-cycle and time iteration procedures in B2-EIRENE
Further explore residual based time stepping and preconditioning techniques for further code speed up
Further conduct 2 approaches towards ITER-runs

## Slide 36: Questions?
or suggestions …
are welcome

## Slide 37: Additional slides
Error assessment
Speed up factors
Success rate for CS
Error assessment Kristel

## Slide 38: Discretization error when CS
Different estimates for discretization order lead to similar results

## Slide 39
Correlation errors
Plasma density Parallel velocity Neutral density
Berekend op basis van residu’s en dan A-1

## Slide 40
For B2-EIRENE (here slab geometry; R=0.3)
Code speed up Assessing speed
Correlation sampling
Converged up to machine precision
Random noise
Not converged

## Slide 41
Kukushkin’s metric behaves similar for CS and random noise
Unless accuracy gets stuck by noise
Code speed up Assessing speed
1D model

## Slide 42
2D test case, slab - CS
Code speed up Assessing speed
Balances for energy are problematic in this case
B2 is well-converged  no balance error
EIRENE unbalance due to track length estimator

## Slide 43
Short cycle, similar behavior for CS and random noise
Code speed up Assessing speed
1D model

## Slide 44: Code speed-up Strict convergence criterion (CS only!)

## Slide 45: Code speed-up Following Kukushkin’s metric

## Slide 46: Success rate for correlated sampling
Success rate decreases with increased complexity: Dimensionality, number of atomic processes, recycling,...
Success rate increases with increased correlation: One seed versus all seeds fixes, fixed source sampling, (fixed trajectories?)
 Improved correlation techniques needed