## Slide 1: Plans for development and release of SOLPS-ITER
X. Bonnin
ITER Organization

## Slide 2: What is SOLPS?
SOLPS : Scrape-Off Layer Plasma Simulation
  A 2D fluid plasma solver (originally B2)
  A kinetic neutral transport solver (Eirene)
Main tool used during the ITER Divertor design
In use by many groups for many devices around the world:
  IO, IPP, Jülich, St. Petersburg, CCFE, VTT, ORNL, IPR, ASIPP, SWIPP, Keio U., NFRI
  ITER, AUG, JET, Alcator C-mod, DIII-D, TCV, MAST, DEMO, SST, EAST, Globus-M, Magnum-PSI, PMTS, …
Part of the EU-ITM strategy for integrated modelling
  Coupling to ASTRA and ETS core transport modules
  Coupling to NCLASS (neoclassical transport)
  Coupling to a PFC heating module
  Possible coupling to kinetic particle codes
Generic geometry support: linear, limiter, SN, DN
Will continue to provide edge/SOL/divertor plasma descriptions for the ITER scenarios

## Slide 3: The various versions of SOLPS
SOLPS versions | Eirene_96 | Eirene_99 (molecules) | Eirene_facelift (MPI parallelization, radiation transfer, triangular grids) | Eirene_2010 (ADAS)
B2 (IO + FZ-Jülich) | SOLPS4.0 |  | SOLPS4.2 | SOLPS4.3
B2.5 (IPP) | SOLPS5.0 |  | SOLPS5.1 | 
B2.5 + drifts (St. Petersburg) | SOLPS5.2 |  |  | SOLPS-ITER

## Slide 4: What will be SOLPS-ITER?
SOLPS-ITER will be the reunion of the various versions of B2/Eirene that currently co-exist
Aims to become the new standard SOLPS version shared by all ITER Members
  Maintained and distributed from the IO
SOLPS-ITER also refers to the run environment around B2/Eirene:
  Grid generation (CARRE/TRIA/TRIAGEOM)
  Case build-up (DG/Uinp/b2yt)
  Real-time and post-run analysis scripts
  Post-processing (b2plot)
  Run archival/retrieval (b2md/b2rd)
  Converters between various SOLPS versions (b2xd/b2sxdr)
  Documentation and manuals

## Slide 5: The SOLPS-ITER data structure
Two main components
  A geometry description
  A description of the plasma edge state
Our model: the EU-ITM GGD and “edge” CPOs
  GGD: Generalized Grid Description
  CPO: Consistent Physical Object
  Being transposed into IDSs (Interface Data Structures) within ITER Data Model
We will also use:
  A standardized A&M database format (AMNS)
  A standardized device description (not just ITER, but also any other device of interest)
Run input and output data files will then be centrally archived within IMAS (Integrated Modelling & Analysis Suite)

## Slide 6: The SOLPS-ITER tree structure
Similar to the existing SOLPS5.1 structure
  Avoid deep directory branches
Thin top layer containing:
  Environment variables setup
  Analysis scripts library
Links to source repositories for DG, CARRE, Eirene & B2
  Allows for parallel development at IO and in Member institutions
  Provided as GIT submodules
  Ensures bug fixes and improvements are accessible to all workflows using them
Large run and data files will not be stored there
  Except those needed for benchmark and regression tests
  Others will go to IMAS archival

## Slide 7: SOLPS-ITER Release plans
A SOLPS-ITER@iter.org mailing list has been created
  60+ members in all ITER parties
  Membership open!
A Release Workshop will take place on April 13-17th, 2015 in Cadarache
  Limited space to ~40 people
  Aimed at experienced SOLPS users (any version)
  Will present:
    The SOLPS-ITER equations and solution benchmarks
    The SOLPS-ITER run environment
    The version control protocols in place (GIT)
    The run and data archival/retrieval procedures
    Sample case build-up
    Practice running benchmark cases
  Will discuss order of new feature implementations and old feature imports

## Slide 8: SOLPS-ITER features
Aimed for at release time:
  Multi-fluid (+bundling), drifts, triangular grids for neutrals
  OpenMP parallelization of B2.5 kernel
  Use of IDS structures for run archival/retrieval to IMAS
  Converters from older SOLPS versions
  Improved feedback schemes
Planned for later delivery:
  Extended grids support
  GUI for easy case build-up/follow-up/analysis
  Coupling to trace impurity following kinetic code (IMPGYRO)
  Coupling to improved PFC heat transfer module
Further suggestions welcome…

## Slide 9: SOLPS-ITER is a community effort
Benchmarks of advanced features with other versions of SOLPS and/or other codes
  N-seeding runs with drifts
  Viscosity effects in magnetic pinches
  Grid sensitivity studies
  Atomic/Molecular/Surface physics sensitivity studies
  …
Establishment of a library of standard cases for all devices interested to serve as a base for future studies
Introduction of SOLPS-ITER as a workflow actor in integrated models
  Core/edge/PFC for overall machine performance
  Edge/sheath/PFC for lifetime and erosion studies
  …
All contributions are welcome!