## Slide 1
GRAY
EC quasi-optical ray-tracing code
for ECRH&ECCD calculations in tokamaks
L.Figini, D. Farina
IFP-CNR, EURATOM-ENEA-CNR Assoc.
Milano,Italy

## Slide 2: Physics model
          l wavelength, w beam width, L system dimension: l << w << L
          asympotic expansion wave equation -> QO cold dispersion relation has additional terms (grad SI) with respect to geometric optics (GO)
            coupled ray equations describing diffraction effects
Gaussian beam:
Propagation of EC Gaussian beams is dealt with in the framework of the compex eikonal approximation
wave equation solution of the form:
S(x) complex eikonal function S = SR + i SI
        beam shape
        beam propagation
Absorption coefficient computed solving either the fully of the weakly relativistic EC dispersion relation
CD efficiency computed using the adjoint method (Cohen model or momentum conservation model from Marushenko, not yet in ITM version)

## Slide 3: Standalone version
Fortran 77 code. Input files:
Magnetic equilibrium description (G EQDSK format)
ne, Te, Zeff profiles
Code parameters (including initial conditions for beamtracing) and options
EC Eq. launcher
EC Upper launcher
JET
E4J project
ITER
D. Farina, L. Figini, NF 50 (2010) 095007 G. Ramponi, et al., NF 48 (2008) 054012

## Slide 4: GRAY on the ITM Gateway
On the ITM Gateway:
subroutine communicating with the calling routine through CPOs (4.08a)
Input CPOs:
  equilibrium
  coreprof
  antennas
Output CPO:
  waves
code parameters stored in XML format, and passed to GRAY in a codeparam structure
Kepler actor is now available
interface
subroutine gray(equilibrium,coreprof,antenna,wave,codeparam)
use euitm_schemas
type(type_equilibrium), pointer :: equilibrium(:)
type(type_coreprof), pointer :: coreprof(:)
type(type_antennas), pointer :: antenna(:)
type(type_waves), pointer :: wave(:)
type(type_param) :: codeparam
end subroutine gray
end interface
<?xml version="1.0" encoding="UTF-8"?>
<?xml-stylesheet type="text/xsl" href="./input_gray.xsl" charset="ISO-8859-1"?>
<parameters>
<code_specific>
<i_warm> 2 </i_warm> <!-- 0=no absorption, 1=weakly rel, 2=fully rel w/ asympt expansion, 3=fully rel w/ num integration -->
<i_larm> 5 </i_larm> <!-- order of larmor expansion -->
<i_eccd> 1 </i_eccd> <!-- 0=no, 1=yes ECCD calculation -->
<i_grad> 0 </i_grad> <!-- 0=raytracing, 1=gaussian beam -->
<n_rad_ray> 11 </n_rad_ray> <!-- radial # of rays -->
<n_ang_ray> 16 </n_ang_ray> <!-- angular # of rays -->
<rho_max> 1.0 </rho_max> <!-- beam truncation radius -->
<ds> 0.1 </ds> <!-- beamtracing step (cm) -->
<n_steps> 8000 </n_steps> <!-- max # of beamtracing steps -->
</code_specific>
<output_control>
<i_rho> 1 </i_rho> <!-- profiles w/ constant 0=dpsi, 1=drhop -->
<n_proj_ec> 501 </n_proj_ec> <!-- points in EC profiles -->
<i_step_proj> 100 </i_step_proj> <!-- beam shape data density -->
<i_step_ray> 5 </i_step_ray> <!-- ray data density -->
</output_control>
<data_adjust>
<i_x_pos> 0 </i_x_pos> <!-- -1=lower, 1=upper, 0=no X-point -->
<psi_ne_bnd> 1.05 </psi_ne_bnd> <!-- density boundary -->
<spline_psi> 0.0001 </spline_psi> <!-- psi smoothing coeff -->
</data_adjust>
</parameters>
will be removed if equilibrium%eqgeometry%boundarytype and equilibrium%eqgeometry%xpts are available

## Slide 5: Equilibrium CPO: B components
B components are computed internally from Fdia and y derivatives:
Results coincide with values in equilibrium%profiles_2d%bphi, %br, %bz
Dierckx routines used for Fdia and y interp., and for y derivatives calculation
Test on shot 5/67 (Helena + equilibrium_augmenter)

## Slide 6: Equilibrium CPO: extrapolation
2 types of mesh for equilibrium%profiles_2d
  Rectangular coordinates (R, z).
  Usually it extends outside LCFS, favourite choice for ray-tracing.
  Straight field lines coordinates (y, c).
  More natural for fixed boundary equilibrium solvers, but it does not provide information outside LCFS.
GRAY needs a smooth transition from vacuum to plasma volume
  y values is needed also outside LCFS
  The type of mesh is guessed from psi values along grid%dim1 and emptiness of profiles_2d%position%r, %z
  If straight field coordinates, grid points are considered as scattered, and an extrapolating spline is computed (Dierckx)
    no constraints, same approach as equilibrium_augmenter?
  Tested successfully on cases 5/64 (y, c), 5/67 (R, z)

## Slide 7: Waves CPO: current status
Power density (dP/dV) and EC driven current profiles (Jtor, J||) written in waves CPO (together with the corresponding integrated quantities P, Itor)
A module should be developed to write coresource CPO from waves

## Slide 8: Waves CPO: still to be done
Shot 5, run 67, t=1.0s
Detailed beamtracing data still written on disk only
Beam trajectory
Evolution along the beam of
  Power
  Wave vector
  Polarization

## Slide 9: Antennas CPO
An antennas CPO is needed to provide the initial conditions for the beamtracing
A complete case with an antennas CPO is not yet available
The module write_ec_ant has been built to fill the antenna_ec part of an antenna CPO
Values used to fill the CPO are read from XML file
A Kepler actor has been generated (no CPOs in, antennas CPO out)
<?xml version="1.0" encoding="UTF-8"?>
<?xml-stylesheet type="text/xsl" href="./input_gray.xsl" charset="ISO-8859-1"?>
<parameters>
<mirror>
<alpha> -5 </alpha> <!-- poloidal angle (deg) -->
<beta> 20 </beta> <!-- toroidal angle (deg) -->
<x0> 830 </x0>
<y0> 0 </y0>
<z0> 34.5 </z0> <!-- mirror coordinates (deg) -->
</mirror>
<beam>
<frequency> 170 </frequency> <!-- (GHz) -->
<power> 2.5 </power> <!-- (MW) -->
<i_mode> 1 </i_mode> <!-- 1=OM, 2=XM -->
<w0_x> 2 </w0_x>
<w0_y> 2 </w0_y> <!-- waist dimensions (cm) -->
<dist_w0_x> 160 </dist_w0_x>
<dist_w0_y> 160 </dist_w0_y> <!-- mirror-waist distance (cm), >0 towards plasma -->
<spot_rot> 0 </spot_rot> <!-- spot ellipse rotation (deg) -->
<phase_rot> 0 </phase_rot> <!-- phase ellipse rotation (deg) -->
</beam>
</parameters>
! initial wave power (MW)
p0mw = antenna%antenna_ec%power%value(iant)*1.e-6_dp
! wave frequency (Hz)
fhz = antenna%antenna_ec%frequency(iant)
! wave mode: sox=-1/+1 -> OM/XM
sox = -dble(antenna%antenna_ec%mode(iant))
! beam shape data
wxt = antenna%antenna_ec%beam%spot%waist(iant,1)*1.e2_dp
wyt = antenna%antenna_ec%beam%spot%waist(iant,2)*1.e2_dp
phiw = antenna%antenna_ec%beam%spot%angle(iant)/cvdr
rcixt = antenna%antenna_ec%beam%phaseellipse%invcurvrad(iant,1)*1.e-2_dp
rciyt = antenna%antenna_ec%beam%phaseellipse%invcurvrad(iant,2)*1.e-2_dp
phir = antenna%antenna_ec%beam%phaseellipse%angle(iant)/cvdr
! antenna position and launching angles
phi0 = antenna%antenna_ec%position%phi(iant)
r00 = antenna%antenna_ec%position%r(iant)*1.e2_dp
x00 = r00*cos(phi0)
y00 = r00*sin(phi0)
z00 = antenna%antenna_ec%position%z(iant)*1.e2_dp
alfac = antenna%antenna_ec%launchangles%alpha(iant)/cvdr
betac = antenna%antenna_ec%launchangles%beta(iant)/cvdr

## Slide 10: Kepler workflow

## Slide 11: Benchmarking
ITM version of GRAY has been benchmarked against the original F77 version
  Test case: ITER standard scenario 2
    Data read from file and passed to the F77 version
    Data read from file, used to fill the corresponding CPO structures and passed to the ITM version
  Results match
Benchmark has started against TORBEAM beamtracing code
  Test case: test machine, shot 5, run 67
  Work in progress

## Slide 12: GRAY vs TORBEAM: preliminary results
Shot 5, run 67, t=0.0s
psi grid interpolation issue?

## Slide 13: Future work
Fill waves CPO with all the available data ( coresource CPO)
Replace physical constants values with ITM_constants module
Use flux averaged quantities from equilibrium CPO, when available (no more need of internal computation)
Test code robustness
  try other shots and machines
Continue benchmarking with TORBEAM
  investigate profiles displacement
  compare approaches to vacuum-plasma transition
Benchmark with TORAY-FOM and TRAVIS when ready
Include momentum conservation method (from Maruschenko) for CD computation also in ITM version
Use SVN for revision control
Write code documentation

## Slide 14: Physics model
asympotic expansion wave equation -> dispersion relation:
  cold dispersion relation
Gaussian beam:
Ns : local cold refractive index OM/XM
solution of the Appleton-Hartree
dispersion relation
Propagation of EC Gaussian beams is dealt with in the framework of the compex eikonal approximation
l wavelength, w beam width, L system dimension: l << w << L
wave equation solution of the form:
S(x) complex eikonal function S = SR + i SI
        beam shape
        beam propagation

## Slide 15: Quasi-optical ray equations
Real and imaginary part of the QO dispersion relation:
        additional terms with respect to
geometric optics (GO) approximation:
 diffraction effects
15
partial differential eq.
coupled to ray eqs.
formally equal to GO ray eqs.
with DR depending also on SI
 ray eqs are coupled together
QO ray equations at dominant order in d
D. Farina, Fusion Sci. Techn. 52 (2007) 154.

## Slide 16: ECRH&CD
Current drive efficiency computed using the adjoint method
X reponse function: Cohen model & momentum conservation model (from Marushenko, not yet in the ITM version)
EC power evolution along the ray
absorption coefficient a computed solving either the fully or the weakly relativistic EC dispersion relation
EC driven current along the ray
D. Farina, Fusion Sci. Techn. 52 (2007) 154.