## Slide 1
Bx-2.1.1: ITER ramp-up and ramp-down
Dick Hogeweij and Giuseppe Calabrò
with inputs from Irina Voitsekhovitch and Florian Köchl
Goals of Program
Comparison C – ILW :
look for identical pairs
differences between C – ILW?
what is missing
what should modelling tell us

## Slide 2: Bx-2.1.1 = ITER-like RU & RD: goals
Dick Hogeweij TF E1E2-Meeting 20 November 2012 2
    Ramp-up: study effect on li and flux consumption of
      Variation of dIP/dt
      Varying density in L-mode
      Varying power in L-mode
      H-mode during RU
    Ramp-down: study effect on li and flux consumption of
      Variation of dIP/dt after H-mode in flat-top with ohmic ramp-down
      Variation of dIP/dt after H-mode in flat-top with H-mode ramp-down
      Reduction of elongation with fast ramp down rate
      [both ohmic and heated ramp-down]
      For all these points: Comparison ILW  C wall

## Slide 3: Ramp-up: identical pairs
Dick Hogeweij TF E1E2-Meeting 20 November 2012 3
    Theme ILW C-Wall Remarks
    Ref.  RU 83223 72504
    Ref. H-mode RU 83224 72512
    (83444)
    Density scan L-mode 83447 72516 Density could no be increased enough;
    (83446) New discharges went to H-mode early
    ICRF pow. scan L-mode 83449 72507 Only 1.5 MW of ICRF could be delivered
    (72509)
    Higher RU rate in  RU 83451 72464
    (83225) (72460)
    Higher H-mode RU rate 83226 --
    What is missing:
    Density scan L-mode
    Lower RU-rate, both  and H-mode

## Slide 4: Ramp-down: identical pairs
Dick Hogeweij TF E1E2-Meeting 20 November 2012 4
    Theme ILW C-Wall
    Ref.  RD 83224 72203
    Ref. H-mode RD 83225 72242
    Higher RD rate in  RD after H-mode FT 83226 74396
    Reduction of elongation in fast  RD 83446 72459
    83447 72462
    83449 72204
    What is missing:
      Slower RD rate in  RD after H-mode FT
      Slower & faster RD rate in H-mode RD after H-mode FT
      Reduction of elongation in fast H-mode RD

## Slide 5: Data analysis and Modelling issues in the comparison ILW  C-wall
Dick Hogeweij TF E1E2-Meeting 20 November 2012 5
    Data analysis issues :
    li evolution  next slide
    flux consumption
    H-mode threshold
    Modelling issues :
    Can q profile evolution be modelled with flat Zeff assumption?  later slide
      C-impurity profiles could give a clue …
    Is flux consumption treated correctly in models?  to be addressed by Florian
    Transport properties during RU and RD
    Propose to concentrate on the pairs given in previous slides,
    Starting with ohmic and H-mode reference shots

## Slide 6: Data analysis – li evolution comparison ILW  C-wall
Dick Hogeweij TF E1E2-Meeting 20 November 2012 6
    Red/Green: Ohmic ILW / Ohmic C-wall
    Blue/Brown: H-mode ILW / H-mode C-wall
    First impression – good match
    Ip
    P_NBI
    q0
    li

## Slide 7: Modelling: TRANSP analysis of JET current ramp up/down discharges started (Irina)
Dick Hogeweij TF E1E2-Meeting 20 November 2012 7
OH discharge 83223
KS3/ZEFH, flat Zeff profile, Be impurity only
Ti=Te, zero toroidal rotation
usual problem with EFIT at low pol
TRANSP Wdia is close to EFIT/WP (or WCDI)
EFIT/q is initial profile at 2.5 s
current diffusion with NCLASS
simulated q0 drops too fast (q0~0.6 at the time of the 1st sawtooth crash)
similar q0 behaviour has been obtained for C wall. Possible solution: Zeff(r)
EFIT Wdia
TRANSP Wdia
EFIT WP&WCDI
TRANSP
Measured
Wdia, MJ
q0_EFIT
q0_TRANSP
KK3
Ipl

## Slide 8: JETTO Modelling – first results (Florian)
Dick Hogeweij TF E1E2-Meeting 20 November 2012 8
Simulation conditions:
fully predictive (ne, Te, Ti, jz)
EFIT equilibrium
L-mode Bohm/gyroBohm model
sawteeth: Kadomtsev model
neutral gas flux feedback control (target density: <ne>)
no impurities, assumption of peaked Zeff
JETTO only simulation of ohmic current ramp-up (#83223, #83225)

## Slide 9
Dick Hogeweij TF E1E2-Meeting 20 November 2012 9
JETTO Modelling – first results (Florian)
#83223 exp
#83223 sim
#83225 exp
#83225 sim
Ipl
ne avg
Te ax
Te avg
li(3)
trends in li(3) well matched
li(3) agreement in absolute values seems to depend strongly on Zeff, radiation (pedestal in H-mode)  impurity modelling