## Slide 1
JET AND JT-60U CURRENT PROFILE MODELLING WITH IDENTITY PLASMA EXPERIMENTS
Identity plasma experiments:
Observations and data analysis
Current diffusion modelling: Data, Tools and Validation
Predictive current diffusion simulations
  Impact of NBI current
  Impact of
  Effects of other externally produced current components (in JET)
Conclusions
OUTLINE
Paula Sirén1, Tuomas Tala1, Gerard Corrigan2, Jeronimo Garcia3, Xavier Litaudon3, Antti Salmi1
1Association Euratom-Tekes, VTT, PO Box 1000, 02044 VTT, Finland
2CCFE, Euratom Association, Culham Science Centre, Abingdon OX14 3DB, UK
3CEA, IRFM, F -13108 St-Paul-Lez-Durance, France

## Slide 2
JET #74740
JT-60U #49469
Dimensionless plasma parameters and profiles
((RB)-1, , ne)
Same size and plasma shape
Identity plasma experiments (2008) 1/4
Matched plasma shapes in identity experiments. P.C. de Vries et al. 2009 Plasma Phys. Control. Fusion 51 124050
Different pressure profile

## Slide 3
Identity plasma experiments 2/4
BEGINNING
t = 3.5 s
BEGINNING
t = 5.0s
Shot pair
#49469 (JT-60U)
#74740 (JET)
was selected due to the reverse initial q
P.C. de Vries et al. 2009 Plasma Phys. Control. Fusion 51 124050
END
t = 6.5 s
END
t = 6.0 s
(Time axis shifted)

## Slide 4
The best match
in the q-profile
Identity plasma experiments – plasma profiles 3/4
The reverse shape has disappeared in JET after 6.0 seconds
BEGINNING
END

## Slide 5
Identity plasma experiments – different properties 4/4
Electron density profiles did not match
q profile in JET becomes flat before 6 seconds
Bootstrap fraction is significant in JT-60U (due to favourable density gradient)
NB current density profile (fraction is approximately same, 22-25%)
From simulation input file
From NCLASS
From ASCOT

## Slide 6
Input data:
JET: Smoothed diagnostic data profiles have been used (cxfm, hrts, eftm). Data profiles every 0.5 seconds.
JT-60U: diagnostic data profiles from 5 time points
Current diffusion: JETTO
G. Genacchi, A. Taroni. Rapporto ENEA RT/TIB/88/5
Neutral beam current density: ASCOT (time-averaged) J. A. Heikkinen et al. 2001 Journal of Computational Phys. 173 527-548
Equilibrium: ESCO
Neoclassical resistivity and bootstrap current: NCLASS
W. A. Houlberg et al. 1997 Phys. Plasmas 4 3230
Current diffusion modelling: Data & Tools & Codes

## Slide 7
Time-dependent ASCOT connected to JETTO Equilibrium: EFTM
Time-averaged ASCOT profile
Fokker-Planck code PENCIL
does not work due to non-desirable interactions with equilibrium code ESCO)
(
Testing of NBI computing options (in JET) 1/2

## Slide 8
The time-averaged (3.5 – 7.0 s) NBI current density profile was selected to the JET current profile studies due to the best comparability with JT-60U (only one NBI current density profile available)
Using time-averaged or time-dependent ASCOT profiles does not cause differences in the results of predictive current simulations
Changes in electron density profiles (gradients) do not cause significant effects to NBI current density profiles calculated by ASCOT
Testing of NBI computing options (in JET) 2/2

## Slide 9
Current diffusion model validation (JETTO)
JT-60U
JET

## Slide 10
Impact of NBI current density
in JET replaced with from JT-60U
in JT-60U replaced with from JET
Impact of electron density profile
in JT-60U replaced with from JET
in JET replaced with from JT-60U
Effect of different density gradients in JET
Effect of added externally produced current components in JET
Case 1
Case 2
Predictive current diffusion simulations
Case 3
Case 4

## Slide 11
Bootstrap current, critical bootstrap current
Steady-state properties can be described by critical bootstrap current
J. Garcia, G. Giruzzi. 2012 Plasma Phys. Control Fusion 54 015009
JET
JT-60U
Bootstrap current
Critical bootstrap current

## Slide 12
JET
JT-60U
NBI fraction
JET 22%
JT-60U 24%
NBI current density profile replaced with profiles JETJT-60U
NBI profile does not have a noticeable effect
Reference simulation with data from #74740
NBI current density replaced with profile of JT-60U
Reference simulation with data from #49469
NBI current density replaced with profile of JET

## Slide 13
profile replaced with profiles JETJT-60U 1/2
JET
JT-60U
Reference simulation with data from #74740
Electron density replaced with profile of JT-60U at t=7.0 s
Reference simulation with data from #49469
Electron density replaced with profile of JET at t = 3.5 s

## Slide 14
profile replaced with profiles JETJT-60U 2/2
6.0 s : 20%
10.0 s: 11%
6.0 s : 33%
10.0 s: 23%
6.0 s : 62%
10.0 s: 42%
6.0 s : 38%
10.0 s: 27%
Bootstrap fractions
JET
JT-60U
Bootstrap current
Critical bootstrap current
Reference simulation with data from #74740
NBI current density replaced with profile of JT-60U
Reference simulation with data from #49469
NBI current density replaced with profile of JET

## Slide 15
q profile time evolution in JET with different profiles (gradients) 1/2
Experimental electron density profile is replaced with density profiles with 5 different density gradients at 3.5 s
Reverse shape stays longer than in the reference but it has been disappeared before 10.0 s in every case (bootstrap fraction has decreased by 32% or less)

## Slide 16
profile replaced with profiles JETJT-60U 2/2 – critical bootstrap current 2/2
6.0 s : 38%
10.0 s: 28%
6.0 s : 43%
10.0 s: 38%
6.0 s : 38%
10.0 s: 28%
6.0 s : 32%
10.0 s: 25%
Bootstrap fractions
Bootstrap current
Critical bootstrap current
Condition of critical bootsrap current is not fulfill any cases after 6.5 seconds

## Slide 17
Effect of added LH (externally produced) current component 1/2
LH current fractions
23% (blue)
31% (red)
9% (green)
Externally generated current density components have added at 3.0 s
Reverse shape stays longer than in the reference simulation but it has been disappeared before 10.0 s in every case (bootstrap fraction has decreased by 38% or less)

## Slide 18
Effect of added LH (external produced) current component 2/2 – critical bootstrap current
Bootstrap current
Critical bootstrap current
6.0 s : 38%
10.0 s: 28%
6.0 s : 43%
10.0 s: 38%
6.0 s : 38%
10.0 s: 28%
Bootstrap fractions
Condition of critical bootsrap current is not fulfill any cases after 4.5 seconds

## Slide 19
Conclusions
The density gradient has the most important role in maintaining the shape of the q profile.
The same density gradient produces larger bootstrap component in JT-60U than in JET. This behaviour is also noticed by studying critical bootstrap current.
The reason why density peaks is not understood and the interaction between the density ITB and sustaining reversed q-profile not known. Self-consistent simulation between predictive density and predictive current profile planned may help to understand the issue.