## Slide 1
1) ITER hybrid scenario modelling with EPED constraints
2) Status on Relaxation of the ITER hybrid-scenario q>1 constraint by sawtooth control

## Slide 2
Extension of IAEA 2012 EPED1 compatible hybrid scenarios
Extension 1: Maintain q>1 constraint by shifting ECCD mirror angles
Expected loss of Pfus due to s/q effect in the x~0.4 region. Runs ongoing (here only t=390s)

## Slide 3
Extension of IAEA 2012 EPED1 compatible hybrid scenarios
Extension 2: Break fGW <1 constraint by peaking ne and maintaining same nped. Hopefully q>1 due to extra bootstrap current
Unfortunately, T drop (due to TEM and/or n dependence in gyroBohm normalized flux) leads to reduced ECCD and NBI current. fni remains the same throughout the scan
Runs ongoing (here only t=500s)

## Slide 4
Initial sawtooth control runs
Motivation: See how tsawtooth /tresisitive can be increased for hybrid-like q-profiles but with q<1. The lower the ratio the more stable (i.e. higher betaN limit) NTMs are to sawteeth. Perhaps hybrids with q<1 but stable NTMs are possible? Would extend greatly operational window of scenario
First step: Feel ‘comfortable’ with Porcelli sawtooth model in CRONOS. Set arbitrary constant in critical shear such that tsawtooth ~ 100s for scenario 2 (H-mode). Then test tsawtooth sensitivity to Ip = 15  11 MA scan, and to sawtooth control with ECCD. Transport is scaling based with H=1.
Energy confinement time much shorter than sawtooth period, therefore pressure perturbations' are on average small
Porcelli trigger model has critical shear dependency of (r(q=1))-4/3 ! Not beneficial for shorter tst but stable for small r
More challenging step later is to include fast particle destabilization/stabilization effects

## Slide 5
Initial sawtooth control runs

## Slide 6
Initial sawtooth control runs
General note: sawteeth effects on average q-profile but not temperature and density profiles. Therefore, the ‘average’ q-profile in between sawteeth more relevant for setting turbulence levels.
Thus, even for standard H-mode, hybrid-like q-profiles with flatter shear in the core apply!