## Slide 1: studying scenarios for West with metis
Clarisse Bourdelle, Jean-François Artaud
and the WEST Scientific Program team
2nd ISM working session
June 3rd 2013

## Slide 2: outline
Analyzing 4 JET pulses with METIS
Summary of “rules” that worked on 4 JET pulses (with different B, fuelling, triangularity)
Applying these rules for 13 WEST scenarios
Conclusions and perspectives

## Slide 3: JET pulses
First pair: 82541 and 82536, with NBI 17MW, Ip=2.5MA, B=2.6T, q95=3.3, high triangularity. The fuelling being 1.6x1022 e/s in 82541 and 4x1022 e/s in 82536
Second pair: 82120 and 82123, with NBI 10.5 MW, Ip=2MA, low triangularity, same fuelling 2.5x1022 e/s, two B: B=2.1T and q95=3.2 (82120); B=2.7T and q95=4.1 (82123)

## Slide 4: Rules used in METIS: energy content
H factor adjusted to reproduce energy content: 0.7 for 82123, 82536, 82541; 0.85 for the lowest B (highest b) 82120

## Slide 5: Rules in METIS: impurities and radiated power
Zeff flat in JET, value as measured ~ 1.3-1.5
Be and C, such that nC/nBe=0.02
W such that nW/ne at separatrix = 10-4
W accumulation factor for W such that nW profiles similar to Mantica 2012
Prad using Post coefficients

## Slide 6: Rules in METIS: radiated power
NB: Cases for 82536 and 82541 where PSOL =0, normal?

## Slide 7: Mantica et al 2012
Using SXR and spectrometers in JET ILW
W slightly hollow with nW max ~ 1.2 1015m-3

## Slide 8: Rules in METIS: W content

## Slide 9: Rules in METIS : Density profiles
In METIS (J-F Artaud, note PHY/NTT-2008.001) the density profile is estimated using the following rules:
  For both L and H modes, the density at the separatrix follows a scaling law based on Mahadavi Phys. Plasmas, such that , where is the volume averaged density.
  Then the peaking of the profile matches scaling laws deduced from JET and AUG databases [Weisen PPCF 2004, Weisen NF 2005] such that:
, with .
    In H mode, the collisionality dependence is chosen [Weisen]:
  pedestal density such that Wped follows Cordey scaling law.
  There are 21 radial points, so the pedestal density is automatically the 2nd point of the profile, i.e. the pedestal width is always 4.8%.
  T is adjusted to match the H factor given

## Slide 10: Rules in METIS : Density profiles

## Slide 11: outline
Analyzing 4 JET pulses with METIS
Summary of “rules” that worked on 4 JET pulses (with different B, fuelling, triangularity)
Applying these rules for 13 WEST scenarios
Conclusions and perspectives

## Slide 12: List of choices made for WEST metis simulations
As for JET pulses:
  Low Zeff=1.3, flat
  density profiles: peaking with neff
  W source (nW/ne at separatrix = 10-4) and same accumulation factor
  Prad using post coefficient
  H98=0.7 (1, and 1.2 explored too)
Additional choices
  LH:
      to optimize accessibility N//=2
      2 densities: one compatible with the cold approximation accessibility: n=6.5 1019m-3, another with an upshift <0.2: n=8.5 1019m-3
      LH deposition at r=0.3 with a width of 0.3 (similar to last high LH power in Tore Supra 2011)
      CD: Goniche scaling law
  ICRH:
      No ripple losses, although expected high (~25%)
      55.5MHz, to have central 1H layer at nominal B
      nj=25
      nH/ne=7%

## Slide 13: List of choices made for WEST metis simulations: ICRH
55.5MHz to have central 1H absorption layer

## Slide 14: List of choices made for WEST metis simulations: LH
N//=2.2
N//=2
Illustration of the LH accessibility formula in the cold approximation
Hard X rays, TS 48161, LH=4MW

## Slide 15: WEST scenarios
Scenario | High power |  |  |  |  |  | standard |  |  |  |  | High fluence | 
Ip (MA) | 0.776 | 0.465 | 0.776 | 0.465 | 0.776 | 0.776 | 0.776 | 0.465 | 0.776 | 0.465 | 0.776 | 0.465 | 0.465
X point height (cm) | 1.7 | 10.1 | 1.7 | 10.1 | 1.7 | 1.7 | 1.7 | 10.1 | 1.7 | 10.1 | 1.7 | 10.1 | 10.1
BT (T) | 3.6 | 3.5 | 3.6 | 3.5 | 3.6 | 3.6 | 3.6 | 3.5 | 3.6 | 3.5 | 3.6 | 3.5 | 3.5
q95 | 3.1 | 4.1 | 3.1 | 4.1 | 3.1 | 3.1 | 3.1 | 4.1 | 3.1 | 4.1 | 3.1 | 4.1 | 4.1
H98 | 0.7 | 0.7 | 0.7 | 0.7 | 1 | 1.2 | 0.7 | 0.7 | 0.7 | 0.7 | 1 | 0.7 | 1
ne (1019m-3) | 8.5 | 8.5 | 6.5 | 6.5 | 8.5 | 8.5 | 8.5 | 8.5 | 6.5 | 6.5 | 8.5 | 5 | 5
fGW | 0.7 | 0.9 | 0.55 | 0.7 | 0.7 | 0.7 | 0.7 | 0.9 | 0.55 | 0.7 | 0.7 | 0.52 | 0.52
Pheat (MW) | 15 | 15 | 15 | 15 | 15 | 15 | 12 | 12 | 12 | 12 | 12 | 10 | 10
LHCD (MW) | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 7 | 7
ICRH (MW) | 9 | 9 | 9 | 9 | 9 | 9 | 6 | 6 | 6 | 6 | 6 | 3 | 3
PL-H (MW) | 6 | 5 | 4.5 | 4 | 6 | 6 | 6 | 5 | 4.5 | 4 | 6 | 3.5 | 3.5
Prad (MW) | 1.70 | 1.59 | 1.04 | 0.96 | 1.74 | 1.74 | 1.72 | 1.61 | 1.02 | 0.96 | 1.73 | 0.58 | 0.59
nW (1015m-3) at r=0.5 | 2.4 | 2.8 | 1.6 | 1.5 | 2.2 | 2.1 | 2.6 | 2.9 | 1.2 | 1.6 | 2.4 | 0.8 | 0.8
r of q=1 | 0.45 | 0.35 | 0.5 | 0.1 | 0.4 | 0.3 | 0.5 | 0.4 | 0.4 | 0.1 | 0.4 | no | no
li | 1.07 | 1.23 | 1.29 | 1.11 | 1.03 | 0.98 | 1.13 | 1.29 | 0.98 | 1.18 | 1.08 | 1.00 | 0.85
bp th | 1.12 | 2.09 | 1.00 | 1.86 | 1.63 | 1.98 | 1.05 | 1.95 | 0.93 | 1.73 | 1.51 | 1.45 | 2.12
Wth (MJ) | 0.64 | 0.40 | 0.57 | 0.36 | 0.91 | 1.09 | 0.60 | 0.38 | 0.53 | 0.38 | 0.85 | 0.29 | 0.41
Bootstrap (MA) | 0.16 | 0.11 | 0.14 | 0.14 | 0.24 | 0.31 | 0.13 | 0.10 | 0.15 | 0.11 | 0.22 | 0.13 | 0.23
LHCD (MA) | 0.18 | 0.14 | 0.25 | 0.20 | 0.21 | 0.23 | 0.19 | 0.15 | 0.25 | 0.22 | 0.23 | 0.33 | 0.38
Flat-top (s) (14 Wb consumed) | 20 | 37 | 36 | 79 | 39 | 62 | 18 | 33 | 30 | 67 | 34 | 227 | recharge

## Slide 16: 15 MW, 0.776 MA, 8.5 1019m-3, H=0.7

## Slide 17: 15 MW, 0.776 MA, 8.5 1019m-3, H=0.7

## Slide 18: 15 MW, 0.776 MA, 8.5 1019m-3, H=0.7

## Slide 19: 15 MW, 0.776 MA, 8.5 1019m-3, H=0.7
Te
ne
Ti
4keV
10.1019m-3
3.2.1015m-3
nW
Tped ~550eV
nped~7.1019m-3

## Slide 20: Pedestal, 15 MW, 0.776 MA, 8.5 1019m-3
H=1
H=1.2
Te
Ti
6keV
Te
Ti
7keV
Tped ~700eV

## Slide 21: Q profiles, H=0.7
q=1 at mid-radius
s always positive
q>1 at all radii
s<0 until mid radius
6 LH + 9 IC MW, 0.776 MA, 8.5 1019m-3
7 LH + 3 IC MW, 0.465 MA, 5 1019m-3

## Slide 22: T and density profiles, H=0.7
Te
Ti
4keV
Tped ~550eV
6 LH + 9 IC MW, 0.776 MA, 8.5 1019m-3
7 LH + 3 IC MW, 0.465 MA, 5 1019m-3
ne
6.1019m-3
ne
10.1019m-3
Te
Ti
4keV
Tped ~600eV
nped~3.1019m-3
nped~7.1019m-3

## Slide 23: ICRH, LH power depositions, H=0.7
PLH
PICRH
PICRH
PLH
6 LH + 9 IC MW, 0.776 MA, 8.5 1019m-3
7 LH + 3 IC MW, 0.465 MA, 5 1019m-3

## Slide 24: WEST T pedestal lower and density ped higher
WEST 15MW, 0.8MA, 8.5 1019m-3 vs JET 82541: more W, higher ne but lower Te for r/a>0.5
WEST, Te
JET, Ti
WEST, nW
WEST, ne
JET, Te
WEST, Ti
JET, ne
JET, nW

## Slide 25: Why Prad low in west?
Because smaller volume! In MW/m3 larger Prad in WEST than JET as expected!
WEST, Prad
JET, Prad

## Slide 26: More corE bootstrap in WEST
bootstrap in pedestal similar, and elsewhere larger in WEST due to higher fraction of trapped
WEST, jboot
JET, jboot
jtot

## Slide 27: outline
Analyzing 4 JET pulses with METIS
Summary of “rules” that worked on 4 JET pulses (with different B, fuelling, triangularity)
Applying these rules for 13 WEST scenarios
Conclusions and perspectives

## Slide 28: Summary of west scenarios
Using 4 JET pulses: chose 10-4 for nW/ne, H ~0.7, hollow W profiles, density peaking and separatrix values
LH deposition arbitrary (based on last TS campaign) 0.3 with a width of 0.3, N//=2
ICRH 7% of nH/ne, 55.5 MHz
With these choices, low level of Prad, but Prad/m3 is higher in WEST as expected due to higher density. But since the volume is smaller, Prad is lower in WEST at most 14%.
Large level of core bootstrap due to large fraction of trapped. Fraction bootstrap max around 1/3
T pedestal weak, density pedestal large
q profiles can be reversed at low density large LH. Or wide region of q<1 for high density cases.

## Slide 29: perspectives
Test impact of W peaking factor on Prad results
Vary ratio nW/ne 10-4 to higher values, compare to COREDIV
Test impact of density scaling on Tped, explore Tped / edge bootstrap range
LH: double issue of CD efficiency and accessibility. Will influence strongly the scenarios. Need LUKE estimates of both
Add ICRH only scenario, at various B
Check consistency of pedestal with MHD peeling/ballooning stability
Compare T and n profiles/pedestals with CRONOS tuned for JET/JT60-U
Estimate LH ripple losses in worse case scenario (low n and high Ip)
ICRH: ripple losses are expected at 25% range. Not accounted for here. Need to estimate using EVE/SPOT type of tool.
ICRH deposition with EVE, power to ions?
MHD stability of q profiles

## Slide 30: Why Prad is low in WEST scenarios? Radiated power from W
http://www-amdis.iaea.org/FLYCHK/ZBAR/csd074.php
Radiated power per volume unit increases with higher electron density and sensitive to Te below 2 keV, not much above
1020m-3
1019m-3