## Slide 1: ITER Integrated Modelling Tools: Status and Outlook
SD Pinches with thanks to M Hosokawa, T Casper and IM Design Team
ITER Organization
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization

## Slide 2: STATUS of ITER Integrated ModeLling Tools (IMAS)

## Slide 3: Integrated Modelling & Analysis Suite
Integrated Modelling & Analysis Suite (IMAS) is the set of tools that will:
  Support operations
    Robust, reliable tools that can be used to validate pulses, perhaps with constraints on runtime
  Support research
    More sophisticated tools that can be used to unpick complex physics questions and address the science coming out of ITER
    These tools can also be used to advance the simpler (perhaps more empirical) tools used to support operations
  Support construction
    Present-day tools that can holistically model the future conditions in ITER to aid and support on-going design questions

## Slide 4: Stages of IMAS Development
2011-2013: Conceptual design, initial infrastructure and physics
  Implement prototype infrastructure (Data Model, workflows, access layer, version control and documentation) and physics models
  Train ITER staff (“alpha users”) to use and evaluate effectiveness
2014-2016: Extend infrastructure and physics
  Complete development of basic workflows and other supporting infrastructure
  Establish fundamental basis for all types of pulse planning
    Plasma Simulator evaluates confinement properties and response to H&CD and fuelling systems
    Coupled PS-PCS system addresses whether the control system has the capability to reach the desired operating conditions using feedback control without violating system constraints
2017-2020: Full Physics for Pulse Planning, begin Reconstruction / Analysis
  Implement broad range of physics components and applications for Pulse Planning
  Physics models will undergo extensive V&V against data from other devices
  Planning for pulse execution, analysis and research commences

## Slide 5: Status of Integrated Modelling
IM Programme now has prototype IMAS Framework:
  Data Model (v0.34)
    Undergoing internal/external review before full adoption
  Data Access
    Physics Universal Access Layer (PUAL)
  Workflow Engine
    Based on Kepler
  Distributed Revision Control System
    Git: Supports simultaneous development in IO and Members
  First simple workflows for Plasma Simulator implemented
    Based on CORSICA
  Example coupling of IMAS-based Plasma Simulator with PCS Simulation Platform

## Slide 6: Status of Data Model and Storage
ITER Physics Data Model standardises data exchange
  Describes both experimental and simulation data
    Many different use cases
  Composed of Interface Data Structures
    Equivalent of ITM CPOs
  Rules & Guidelines underpinning Data Model
    Externally reviewed
    Presently internally reviewing
Temporary database for storage
  Links to on-going work within CODAC on ITER Archiving

## Slide 7: Training
Training (14th February, 18/19th February, 7th March)
  6 half-day sessions to familiarise IO staff with prototype installation
IO has now integrated CORSICA into IMAS and implemented first workflows
  Fixed boundary, core transport
  Free boundary

## Slide 8: Infrastructure: Revision Control
IM Programme will benefit from using a distributed revision control system for all components
  Parallel development in IO and ITER Members
  Git selected
Gitorious being trialled to manage development
  Merge changes
  Code review

## Slide 9: Plasma Simulator for PCS Evaluation
Started development of Plasma Simulator (PS) to test, refine and extend Plasma Control System (PCS)
  CORSICA integrated into IMAS
Coupled PS-PCS Simulation Platform will form basis for pulse preparation and validation
  High priority application for prototyping IM infrastructure
  Successfully demonstrated prototype coupling in a co-simulation of IMAS and PCS-SP

## Slide 10: Interfaces in coupling IMAS Plasma Simulator to PCS Simulation Platform

## Slide 11: Development of CORSICA Workflow
First “Plasma Simulator” workflow created with support from IM Design Team
  CORSICA integrated within IMAS Workflow Engine (Kepler) as a complete entity
  Execution of Workflow controlled from within Workflow Engine
  Data exchanged (imported/exported) via Remote Procedure Calls (RPC)
  Initially, two cases considered: Fixed boundary core transport & free boundary simulation
  CORSICA dispatched remotely from Workflow Engine (ssh)
  CORSICA output stored in IMAS Database using ITER Physics Data Model
  IDSs stored each time step: Core Profiles, Equilibrium and PF Coils
  Scenario evolution can be examined/plotted during run
  Workflow uses mixed language actors coded in C/C++ and Fortran90
Over course of this year extend workflow to couple to PCS Simulation Platform
  Co-simulation with Simulink-based PCSSP
Workflow and Actors version controlled using Git (access controlled)
  git clone [username]@hpc-login4.iter.org:/work/repos/git/corsica-kwf.git

## Slide 12: Overview of CORSICA Workflow
Initialise IMAS Database (with “ualinit”)
Start CORSICA RPC Server on remote machine (using ssh) (t = t0)
Communicate with CORSICA (using BASIS*) to advance to t = t + tadv and retrieve evolved data (t = t0 + tadv)
Store data in IMAS Database using “ualslicecollector”
Loop back to step 3 if t < tend
Terminate CORSICA server
Finalize IMAS Database with “ualclose”
Kepler & Actors on HPC login node
[hpc-login4.iter.org]
IMAS Infrastructure
corsicainitialize
corsica
corsicaparse
corsicaterminate
CORSICA Server on HPC Cluster
[c01b01.iter.org – c01b04.iter.org]
BASIS
CORSICA modules
eq
SSH
RPC
ctr
csc
rpc
* BASIS is a scientific programming language developed by LLNL and a development environment providing with an interpreter, graphics, terminal logs, etc.

## Slide 13: CORSICA Workflow in Kepler
M Hosokawa & T Casper

## Slide 14: CORSICA Workflow During Execution
M Hosokawa & T Casper

## Slide 15: Comparison with standalone CORSICA
Shape evolution from plasma limited on inside wall (TRANSMAK result) to a diverted plasma with initiation of auxiliary heating after plasma diverts
Results are from “backing out” mode of simulation that uses a prescribed boundary evolution followed by a free-boundary calculation at each time step to evaluate system constraints
  e.g. Coil current and field limits and forces on coils
M Hosokawa & T Casper

## Slide 16: Comparison with standalone CORSICA
M Hosokawa & T Casper

## Slide 17: Comparison with standalone CORSICA
M Hosokawa & T Casper

## Slide 18: Outlook for ITER Integrated ModeLling Tools

## Slide 19: Future Work
Data Model
  Finalise Rules & Guidelines for ITER Physics Data Model
  Agree release versions of IDSs
    Equilibrium, Core Profiles, PF, …
  Encourage use for ITER modelling work
    ITPA, ISM,…
Plasma Simulator for PCS Simulation Platform
  Extend IMAS Plasma Simulator (CORSICA workflow) to couple with PCS Simulation Platform
Workflow Engine
  Improve performance

## Slide 20: Future Work
Integrate other physics codes
  Start to develop workflows based around ASTRA and DINA
  Licencing and MoUs
Access Layer and Archiving Database