Optimisation of operational space for long-pulse scenarios

in support of ITER Physics Operation Workprogram (DT-phase)

Proposals: 	were formulated in the report at ISM WS 19 Jan 2011

ISM response: dig the existing data which can contribute to the task to understand 					whether the data are sufficient or new simulations are required

TASK:

Assessment of operational space (OS) for long-pulse scenarios by 1.5D modelling

= Basic goal:

To find the OS for long pulse operation tFT > 1000 s, Pfus > 250 MW

= Scope of the task:

To provide scan of current and density: Ip = 8 -15 MA, n = 3 1019m-3 - nG;

-  	for ITER set of H&CD: 16.5 + 16.5 MW NBCD+ 20 ECCD (+ 20 ICCD)

-	for each of the transport models keeping the transport assumptions used 					for baseline 15 MA simulations (for existing data analyses by ISM transport 					assumptions can be different from Ip=15 MA case. Then the comment what

was modified and why is required).

I. For those who already have data for long-pulse (please fill the lists):

Input data (please specify the model used for core transport and pedestal):

-	Description of plasma configuration if different from full bore baseline case:

BxR = 5.3x6.2 Tm; a/R=2/6.2 m, ka=1.76 (ka = S/a2), triangularity ~ 0.5,

-	Description of the set and configuration of the H&CD:

NBI: 	PNBI,on-axis =	 			PNBI,off-axis=				,MW

ECCD:  	PEC,co, MW =	 			location = 			width=

ICCD:	PIC, MW	    =				location = 			width=

(location and width in terms of SQRT(Norm.toroilal flux))

-	Global input variables:

Ip, MA 							=

<n> (volume averaged), 1019m-3, 	=

[n] (chord averaged, 1019m-3, 		=

Output data (please fill the lists):

Required minimal list:

Global	POH = 		Paux = 		Pfus =  		Prad  =			[MW]

Wth =		 Wtot =		 							[MJ]

Zeff, = 		nBe/ne=		nHe/ne=		nAr/ne=		impurities sort/fractions

N			p =			li	 =

Profile	q(0)=		qmin=		q95 	=

nD+T(0)/ne(0) 	=

Desirable list (if available):	<T>n =<Tn>/<n>

Profile: 	ne(0)	=		<ne> =		 	ne,ped=			ne, edge=			1019m-3,

ni(0)	=		<ni> 	=		 	ni,ped =			ni,edge =			1019m-3,

Ti(0)	=		<Ti>n =		 	Ti,ped =			Ti,edge =			keV,

Te(0)	=		<Te>n=		 	Te,ped =			Te,edge =			keV,

p(0)	=		<p> 	=		 	pped 	=			pedge =			keV*1019m-3

Desirable list (if available):

Pedestal: 	N,ped =			ped =		(=ped/a ?, =ped/a? ,  please mark)

p,e,ped =			*ped=

Derivatives: 	PSOL = POH + Paux + Pfus/5 - Prad

H-mode quality, 		PSOL/PL-H	 	=			PL-H (Y. Martin 2008);

Fusion gain factor, 	Q 			=			(Pfus/( POH + Paux));

Confinement quality, 	H y2,98 		= 			E/E,y2,98;

Flat-top length,  		tFT  [sec]	= 			(240 - 14 Ip) Ip /POH;

II. For those who plan new modelling for long-pulse:

For those who have Ip=15 MA, 500 MW, Q = 10, tFT=400 s

ITER baseline scenario with his/her specific favourite model (CDBM, MMM, GLF23, BgB, etc):

(1) Keep the same input and assumptions you used to simulate 500 MW baseline scenario:

Ip=15 MA, Paux = 50 MW (53 MW?), geometry, pedestal, etc;

(preferably 16.5 MW innermost + 16.5 MW outermost NBI + 20 MW outermost ECCD (EL))

(2) Do density scan by density reduction (lower limit n > n NBI,shine ~ 3 1019m-3)

- 	keeping pedestal pressure (nTe~36 keV*1019m-3 , ped/a ~0.04) and

-	keeping the boundary conditions (ne,edge = 3 1019m-3, Tedge ~ 0.25 keV (level of saturation 		predicted by SOLPS with PSOL ~ 100 MW)

(3) For each point of the scan provide the output listed above

(4) Arrange the input and output data as it is shown above

Expected result:

- Pfus and Q can drop (250 MW and Q =5 are still acceptable for hybrid long pulse operation ), 	but pulse length will increase due to increase of the CD efficiency (~T/n) and increase of 	current conductivity (1/Res~ T3/2)

- long-pulse operation at Ip=15 MA is less demanding for transport enhancement, H~1/Ip