## Slide 1
Corsica simulation of ITER hybrid mode operation scenario
S.H. Kim and T.A. Casper
ITER Organization, St Paul lez Durance, France
Acknowledgement : LLNL, ITER/Monaco
R.H. Bulmer, L. LoDestro, W. Meyer and D. Pearlstein (LLNL) – Corsica collaboration
J. Garcia (CEA), M. Henderson (ITER), C.E Kessel (PPPL) and T. Oikawa (ITER)
– useful discussions

## Slide 2: Introduction & outline
Source modules for Corsica simulation
Backing-out simulation of ITER hybrid mode operation
Forward simulation of ITER hybrid mode operation
Summary and perspectives
Simulations of ITER hybrid and steady-state mode operations are requested to support several tasks for resolving ITER physics and engineering issues.
  Feasibility of achieving physics goals, such as Q and plasma burn duration
  Heating and current drive requirements, and profile tailoring
  Plasma control system, coils and power supplies
Realistic source modules (NB/EC/LH/IC) are recently either upgraded or added, and their operating parameters are determined reflecting recent ITER design changes.

## Slide 3: Corsica source modules
NB : Nfreya, MC code for heating and current drive, an existing module in Corsica package, updated beam parameters (T. Oikawa)
EC : Toray-GA, ray-tracing wave code, v1.8 (GA, R. Prater), 5 EC launchers, updated launcher parameters (M. Henderson),
  3 EL , co-EL (upper, 1), counter-EL (middle, 2) and co-EL (lower, 3), and 2UL, USM (4) and LSM (5). Each launcher can deliver 6.67MW .
  Automatic scan on the poloidal and toroidal angles has been developed to find required mirror angles.
LH : LSC, ray-tracing wave code (NTCC), TSC ITER simulation setting (C. Kessel)
ICRF : Toric, Full wave code, in preparation
  A version originally used for developing interface is working, but prescribed heat deposition profiles are used in this work.
  No IC driven current is assumed.
  ITER will have an official version soon from IPP (discussed with R. Bialto and J. Wright)

## Slide 4: Reference simulation of ITER hybrid mode
12.5MA scenario has been developed by tailoring the 15MA scenario (T. Casper)
Large bore startup (initially inboard limiter configuration)
ne(0,flat-top)=8.5e19 m-3 & nGW~9.9e19 m-3
Zeff(t)~1.7+2.3*(ne0(t0)/ne0(t))^2.6 (V. Lukash)
1300s of current flat-top
60s ramp-up without pre-magnetization (XPF at about 15s and L-H transition at 40s)
210s ramp-down (H-L transition 70s after EOF, no auxiliary power 30s after H-L transition)

## Slide 5: Evolution of plasma profiles
Coppi-Tang transport model with the coefficients used for 15MA H-mode simulation
Te(ped) ~ 3-4keV, ρtor(ped) ~0.95
Be and Ar impurity densities, self-consistently with Zeff(t)
33MW of NB (off-axis) & 20MW of EC (2 co-ELs and 1 UL-LSM). Source profiles are calculated at every time-step.
Effective sawteeth by increasing the heat conductivities and plasma resistivity inside the inversion radius, when qmin<0.97

## Slide 6: Evolution of plasma parameters
At t=1359s (tEOF = 1360s)
Q ~ 9.6 & Pα ~ 101MW  high Q (>5.0) with relatively low Paux=53MW
H98 ~ 1.24 & li(3) ~ 0.75  improved confinement, good for the vertical stability
βN ~ 2.5 & βp ~ 0.82  high betas
IBS ~ 3.8MA, INB ~ 2.5MA & IEC ~ 0.4MA  fNI ~ 0.54 (it seems not enough for q>1.0)
q(0) ~ 0.98 & qmin ~ 0.97  a slightly reversed or flat q profile inside ρtor ~ 0.4

## Slide 7: Evolution of coil currents
CS coil currents are well within the coil current limits.
PF6 coil current is briefly violating the coil current limit (~19MA at Bmax = 6.5T without 0.4K sub-cooling ) at SOF. This is OK with UFC criteria.
PF2 coil current is violating its lower coil current limit during the ramp-down, due to the shape transition to the outboard limiter configuration (will be shown later).
The total flux consumption is well within the limit.

## Slide 8: B-field, imbalance current and force limits (Ref.)
PF2 violated B-field, force and imbalance current limits during the ramp-down at about Ip~3.5MA with Paux=0W.
It appears that PCS can handle this with no damages on the system.

## Slide 9: Low density/low confinement/no Sawtooth
Application of different simulation conditions
Low density case
  (ne(0,flat-top) = 7.0e19 m-3 (ne/nGW~0.7)
  lower Wth, H98, βN, βp, Pα, Q and IBS
  higher li, INB and IEC
Low H-mode confinement case
  Slightly higher L-mode confinement (Coppi-tang coef. 2.52.0) and slightly lower H-mod confinement (Coppi-tang coef. 1.101.15)
  lower H98, βN, βp and higher li
No Sawteeth case
  Very similar to reference simulation except q < 0.97
Slightly different q(0) behaviours
At SOF (t=1359s) | Ref | Low dens. | Low conf. | No ST
Wth [MJ] | 361.3 | 296.6 (▼) | 339.9 | 361.4
H98 | 1.237 | 1.187 | 1.185 | 1.238
βN | 2.516 | 2.111 | 2.368 | 2.517
βp | 0.815 | 0.685 | 0.768 | 0.815
li(3) | 0.745 | 0.787 (▲) | 0.741 | 0.745
q(0) | 0.982 | 1.396 | 1.376 | 0.845
qmin | 0.971 | 0.971 | 0.970 | 0.969
min(q) | 0.970 | 0.970 | 0.970 | 0.845
IBS [MA] | 3.76 | 3.05 | 3.57 | 3.76
INB [MA] | 2.49 | 3.22 | 2.36 | 2.49
IEC/ILH [MA] | 0.41/- | 0.50/- | 0.41/- | 0.41/-
Pα [MW] | 100.9 | 68.5 | 92.2 | 101.0
Ploss [MW] | 116.7 | 94.3 | 110.7 | 116.7
Paux [MW] | 52.30 | 52.94 | 52.64 | 52.30
Q | 9.64 | 6.46 | 8.74 | 9.65
Te(0) [keV] | 28.71 | 27.07 | 27.34 | 28.97
Ti(0) [keV] | 29.31 | 27.84 | 27.14 | 29.24
Te(0.95) [keV] | 3.56 | 3.72 | 3.41 | 3.59
Flux(t=7.33s) [Wb] | 69.89 | 69.89 | 69.89 | 69.89
Flux(SOF) [Wb] | -90.22 | -90.90 | -93.27 | -90.22

## Slide 10: Premagnetization
At SOF (t=1359s) | ref | Pre-mag20 | Pre-mag40
Wth [MJ] | 361.3 | 361.5 | 361.4
H98 | 1.237 | 1.238 | 1.238
βN | 2.516 | 2.517 | 2.518
βp | 0.815 | 0.815 | 0.815
li(3) | 0.745 | 0.743 | 0.738
q(0) | 0.982 | 0.975 | 1.041
qmin | 0.971 | 0.970 | 0.974
min(q) | 0.970 | 0.970 | 0.974
IBS [MA] | 3.76 | 3.77 | 3.78
INB [MA] | 2.49 | 2.49 | 2.49
IEC/ILH [MA] | 0.41/- | 0.41/- | 0.41/-
Pα [MW] | 100.9 | 101.0 | 101.0
Ploss [MW] | 116.7 | 116.9 | 116.8
Paux [MW] | 52.30 | 52.41 | 52.30
Q | 9.64 | 9.63 | 9.65
Te(0) [keV] | 28.71 | 28.91 | 29.05
Ti(0) [keV] | 29.31 | 29.27 | 29.10
Te(0.95) [keV] | 3.56 | 3.59 | 3.61
Flux(t=7.33s) [Wb] | 69.89 | 49.69 | 29.50
Flux(SOF) [Wb] | -90.22 | -110.25 | -130.23
Avoiding CS coil lower limits (consuming less flux)
Early H&CD or large bore start-up
Modified shape evolution (flux consumption re-distribution)
Avoiding PF coil upper limits (consuming more flux)
Late H&CD or small bore start-up
Slow current ramp
Modified shape evolution
Application of premagnetization (either 20Wb or 40Wb)
  Very similar plasma parameters with the reference simulation
  Different initial flux state, but similar flux consumption
  Different coil current evolutions

## Slide 11: Coil current and flux state evolution
Pre-magnetization using CEQ package in CORSICA
PF6 coil current limit is avoided with premagnetization
Shift of the flux state, no additional flux consumption

## Slide 12: Application of various HCD schemes
At SOF (t=1359s) | Ref NB33/EC20 | NB33/EC40 | NB33/EC20/IC20 | NB33/EC20/LH20 | NB33/EC20/LH20/IC20 | EC40/LH20 | EC40/IC20
Wth [MJ] | 361.3 | 389.0 | 391.2 | 390.0 | 416.4 | 373.4 | 379.7
H98 | 1.237 | 1.264 | 1.262 | 1.262 | 1.284 | 1.253 | 1.263
βN | 2.516 | 2.709 | 2.722 | 2.712 | 2.888 | 2.500 | 2.545
βp | 0.815 | 0.877 | 0.881 | 0.880 | 0.937 | 0.810 | 0.807
li(3) | 0.745 | 0.723 | 0.715 | 0.622 | 0.592 | 0.655 | 0.722
q(0) | 0.982 | 1.035 | 0.959 | 1.219 | 1.319 | 0.972 | 0.972
qmin | 0.971 | 0.987 | 0.970 | 1.087 | 1.209 | 0.970 | 0.971
min(q) | 0.970 | 0.986 | 0.959 | 1.087 | 1.208 | 0.970 | 0.971
IBS [MA] | 3.76 | 4.09 | 4.10 | 4.30 | 4.65 | 4.06 | 3.95
INB [MA] | 2.49 | 2.65 | 2.62 | 2.68 | 2.72 | - | -
IEC/ILH [MA] | 0.41/- | 0.82/- | 0.41/- | 0.41/0.90 | 0.41/0.89 | 0.82/0.90 | 0.82/-
Pα [MW] | 100.9 | 110.7 | 115.7 | 111.6 | 124.7 | 102.5 | 108.4
Ploss [MW] | 116.7 | 142.9 | 148.7 | 143.9 | 173.8 | 123.7 | 130.2
Paux [MW] | 52.30 | 72.64 | 72.65 | 72.64 | 92.31 | 59.99 | 59.99
Q | 9.64 | 7.63 | 7.97 | 7.69 | 6.76 | 8.53 | 8.93
Te(0) [keV] | 28.71 | 31.61 | 31.43 | 31.32 | 32.74 | 29.85 | 30.31
Ti(0) [keV] | 29.31 | 30.96 | 31.96 | 30.68 | 33.05 | 29.40 | 30.38
Te(0.95) [keV] | 3.56 | 3.84 | 3.83 | 3.94 | 4.04 | 3.77 | 3.70
Flux(SOF) [Wb] | -90.22 | -82.91 | -84.69 | -74.79 | -70.87 | -87.79 | -96.35
53MW (ref)
73MW (ref + 20MW)
93MW (ref + 40MW)
60MW (no NB, 2*PEC)
LH  lower li, q>1.0
Higher Ini  lower flux consumption
Higher power  higher IBS, Pα and lower Q
No NB (2*PEC) cases similar to the reference simulation

## Slide 13: q profile evolution & Flux consumption
Higher non-inductively driven current and heat deposition
  higher q values with LH driven off-axis currents, q>1 until the end of flat-top
  less flux consumption and resulting modifications on coil current evolutions
Higher power but less driven current (EC40/IC20 case)  more flux consumption
t=1359s

## Slide 14: Ramp-down shape evolution
Application of different shape evolution during the ramp-down phase  No violation of coil current, field, force and imbalance current limits
Difficulties on positioning the sources (too peaked current profile)
Limited or diverted configuration ?

## Slide 15: Forward simulation of the reference case
Forward simulation has been done using the reference coil current obtained from a backing out simulation (ICS1 = ICS1U+ICS1L, IPF6 is OK with UFC criteria, PCS might handle IPF2 @ Ip~3.5MA with Paux=0W).
Coil voltages are computed using the ITER controllers (JCT2001 + VS1) and power supply models.
1
2
3

## Slide 16: Voltage evolution
Saturation voltage per turn is used for slow controller, whereas VS1 uses the total saturation voltage, 6kV.
Each coil and saturation voltages are multiplied by its coil turns for plotting (might be not exact)

## Slide 17: Summary and perspectives
  ITER hybrid operation scenario has been simulated using Corsica and realistic source modules.
    Operation space study with different conditions
    Studying optimum source combinations for achieving q>1 condition
  Additional source/pedestal modules
    Official version of TORIC (IPP)
    IC module in ACCOME (long-term ?)
    A pedestal model based on stability analysis
  ITER steady-state operation scenario modelling
    Developing ITER steady-state operation scenarios
    Studying physics issues related to the steady-state operation and ITBs
    Investigating requirements for ITER H&CD systems
  Support ITER PCS and IM projects
  ISM relevant joint activity ?

## Slide 18
Additional slides
1.0

## Slide 19: Automatic scan on EC angles
Automated suggestion for mirror angles of ELupper
Off-axis
High JEC
Pe, EC
JEC

## Slide 20: Realistic source profiles
NB33/EC20/LH20/IC20 case
NB : 33MW, off-axis
EC : 20MW, off-axis, election heating
IC : 20MW, 46MHz (J. Garcia, on-axis Pe & off-axis Pi) / 53MHz (on-axis Pe & Pi) , prescribed heat deposition porifiles, no driven current
LH : 20MW, n||=2.2(C. Kessel), far off-axis
t=60s
t=60s

## Slide 21: Central q behaviours
Reference case
Low density case
Low H-mode confinement case
No sawteeth case
Effective sawteeth increased the plasma resistivity inside the inversion radius  q(0)>1.0
Large jumps at the start of Sawteeth, due to already slightly reversed q profiles
(a)
(b)
(c)
(d)

## Slide 22: Ramp-down shape evolution - limits
No violation of coil current, field, force and imbalance current limits